## Slide 1: Thermodynamic Diffusion Coefficient
A penetrating molecule moves with velocity ux [m/s] in the x direction through a polymer because of a gradient of chemical potential ¶m/¶x [Joule/m]. This gradient is able to overcome the resistance of the medium in a similar manner to the viscous friction in the Stokes law, and, more generally, in fluid dynamics
Indicating with f a friction factor and mT a coefficient of mobility. G is the Gibbs free energy and ni and nj moles of any chemical species (i.e. dn= change in the number of particles)
The negative sign means that the movement is in the direction of decrease of the chemical potential. The movement ceases when ¶m/¶x = 0, that is the equilibrium condition.

## Slide 2: Thermodynamic Diffusion Coefficient
The amount of penetrant dQ that passes through the unit area in the time dt is:
  dQ=C ux dt [moli/m2]
C is the concentration (mol/m3) in the polymer.
The molar flow J=dQ/dt = C ux= -mtC ¶m/¶x
¶m/¶x = ¶/¶x(¶G/¶ni) represents the gradient (driving force) that determines the mobility of the molecules against the resistance of the medium
The thermodynamic diffusion coefficient DT is the kinetic parameter that measures how quickly the molecules of the permeating gas are moving in the diffusive medium. Indicating with J the 1D flow through a membrane, DT ( m2/s) is defined by the relation:

## Slide 3: Thermodynamic Diffusion Coefficient
But by definition with mo the chemical potential in the standard state and replacing:
At equilibrium the activity and the chemical potential in the polymer and in the external phase are equal
The definition of solubility is S=C/a and therefore:
Indicating with P the permeability P=DTS
For a homogeneous medium whose properties do not vary with time DT = constant

## Slide 4: Relation between the two diffusion coefficients
The Fick coefficient is obtained from
C= aS and therefore
For an ideal system (S=cost) S is not function of x and remembering that we defined DT from:
As the two flows are equal :
and if S=cost DT=D

## Slide 5
DIFFUSION IN GLASSY POLIMERS
In the case of glassy polymers (for which is no longer valid the Henry's law), the transport of matter is still related to the Fick's law, but in the equation of transport of the term relative to the adsorption in the cavities must be taken into account.
The accumulation term in the mass balance becomes :
Correspondingly, the mobility of the absorbed or adsorbed molecules into the microcavities will be different: two diffusion coefficients, DH (Henry) and DL (Langmuir) can be defined.
It is assumed, however, that the adsorbed molecules have no mobility so DL =0 and the I Fick’s law becomes:
J = - DH ¶ CH/ ¶ x

## Slide 6
DIFFUSION IN GLASSY POLYMERS
The mass balance becomes:
(1)
Since both the concentrations depend on a, one concentration can be expressed as a function of the other: a is obtained (or equivalently p) by the Henry’s expression and then replaced in that of Langmuir:

## Slide 7
The mass balance will therefore take the following form:
where:
In this form of the mass balance Dapp ,lower than DH being a(CH)<1, depends on the unknown function CH  the differential equation is not linear and it is a non-ideal Fickian case.
Then, it is possible only a numerical solution, once the values of the parameters relating to the absorption are known .

## Slide 8
The balance is simplified in the case in which the isotherm is linear. For example, in the case of absorption at low pressure (b a << 1):
(2)
An expression equivalent to the classic II Fick's law, where κ’=1+CL’b/S is a constant of proportionality, is obtained
Note in particular the disappearance of the dependence of DH on the concentration, which enables to solve the (*) also analytically.
The apparent diffusion coefficient κ’ >1 and Dapp<DH 
expresses from a physical point of view the delay on the transport determined by the accumulation of penetrant in the cavities, when these have not yet saturated.
Substituting CL in eq. 1

## Slide 9
The balance is simplified also in the case in which (b a >> 1). In this case CL+CH=Sa+C’L and the mass balance becomes once again ideal Fickian type:
ba<<1
P(o a)
C
ba>>1

## Slide 10
If the mobility (albeit reduced) is assumed even for molecules adsorbed in microcavities, a dual-sorption dual-mobility model is obtained
The mass balance becomes:
In order to reduce the unknown functions from two to one, CL can be expressed as a function of CH combining the relations of Henry and Langmuir
DIFFUSION IN GLASSY POLIMERS
Dual Sorption-Dual mobility

## Slide 11
Solutions of the mass balance and determination of S, D and P
Experiments of absorption and desorption
If the equation derived from the mass balance is solved analytically, the diffusion coefficient (real or apparent) can be obtained using its simplified solution. For example, for a planar geometry in the case of absorption and desorption from an environment at constant concentration :
I.C. Ci(X,t)=Co t=0 x=[+l]
B.C. C(-l,t)=C’o t>0
C(l,t)=C’o t>0
2l
x
0

## Slide 12
Notes:
In the case of absorption: C’o > Co or Co =0
In the case of desorption: C’o < Co or C’o =0
2l
x
C’o
C’o
Co
2l
x
C’o
C’o
Co
0
0

## Slide 13
The solution of the mass balance with the indicated boundary conditions is given for C as:
Integrating with respect to x:
The solution is given as a sum of infinite terms in two forms, adopted to calculate D in at beginning of absorption or at beginning of desorption experiments:
where Mt is the mass absorbed at time t and M is its asymptotic value.
Solution with the Laplace transforms
Solution by separation of variables
Solution by separation of variables

## Slide 14
The expression (a) allows to describe the early stages of absorption (or desorption) in a simplified form :
For a non-ideal Fickian system, though D is not constant, a linear plot of
Mt/M¥ vs. t0.5 is still obtained
t0.5
Mt
M¥

## Slide 15
The expression (b) is adopted in a simplified form to represent the final stages of the absorption (or the initial stages of desorption ):
plotting ln (1-Mt/M ¥) as a function of the time:
t
ln (1-Mt/M ¥)
ln(8/p2)
For a non-ideal Fickian system, although D is not constant, a linear plot is still obtained.

## Slide 16: Example: drying of a pellet
For PET and PA, drying before to any process that involves the fusion is essential. For PET, drying must be pushed up to 50 ppm of water corresponding to 0.005% by weight.
The boundary conditions are typical of the desorption. The equations in Cartesian and cylindrical coordinates for D = const
2l
x
C’o
C’o
Co
0

## Slide 17: Dimensionless analysis
The balance equations can be easily made dimensionless by placing:
c*=(c-c’o)/(co-c’o)
x*=x/l
t*=t/t
The time t is a characteristic time of interest for the process that is being studied. It can be regarded as an observation time during which diffusion occurs. For example, in this case:
  The time limit of exposure to high T of the polymer to avoid its degradation
  The acceptable time for the transit of the polymer in a drying plant before of an injection molding process

## Slide 18: Dimensionless analysis
With these dimensionless variables the mass balance becomes:
And the dimensionless number Dt/l2 represents:

## Slide 19: Dimensionless analysis
If Dt/l2<<1 then the reference time is much smaller than the diffusion time. In this case, the diffusion process is much slower than that of interest and the concentration Co will be characterized over time t by strong gradients between the center and edges of the pellet.
If Dt/l2>>1 then the reference time is much higher than the diffusion time. In this case, the diffusion process is much faster than the reference time.
The concentration Co will reach values close to
C’o whithin the time t
If Dt/l2=O(1) the balance must be solved.
2l
x
C’o
C’o
Co
0
1
2

## Slide 20: Drying of a PET granule: Dt/l2>>1
Temperature, °C | DPET (m2/s ) | Dt/l2 with t=100 s l=1mm | Dt/l2 with t=1000 s l=1mm | Dt/l2 with t=1000 s l=0.5mm
20 | 7.55E-12 | 7.55E-04 | 7.55E-03 | 3.02E-02
40 | 1.90E-12 | 1.90E-03 | 1.90E-02 | 7.60E-02
60 | 4.20E-11 | 4.20E-03 | 4.20E-02 | 1.68E-01
70 | 8.60E-11 | 8.60E-03 | 8.60E-02 | 3.44E-01
80 | 1.00E-09 | 1.00E-01 | 1.00E+00 | 4.00E+00
100 | 2.00E-09 | 2.00E-01 | 2.00E+00 | 8.00E+00
120 | 3.10E-09 | 3.10E-01 | 3.10E+00 | 1.24E+01
140 | 5.00E-09 | 5.00E-01 | 5.00E+00 | 2.00E+01
160 | 7.80E-09 | 7.80E-01 | 7.80E+00 | 3.12E+01
180 | 1.20E-08 | 1.20E+00 | 1.20E+01 | 4.80E+01
Tg

## Slide 21: Summary
The specimen geometry is critical for measuring D (flat plate: ratio
side / thickness at least 20)
For measurements of S, just the maximum amount absorbed is relevant, and therefore the geometry of the sample is not relevant.
Ideal Fickian system:
  D is measured by an absorption test and plots of Mt/ M¥ vs. t0.5/l are linear
Non-ideal Fickian system D(C):
  Linear plots are obtained as in the ideal case but a coefficient D which is an average between D(C’o) and D(Co) is measured.
  Absorption and desorption do not follow the same behaviour.
Non-Fickian systems :
  The initial part of the plot Mt/M¥ vs. (t)0.5 is not linear
  A plot of Mt/M¥ vs. t0.5/l changes with l
The solubility coefficient can be obtained from the measurement of M¥ .
  M¥ .=2 A l ½ C’o - Co ½ = 2 A l S½ a’o - ao ½ if S is constant

## Slide 22: Indirect measure of the concentration of water
It is possible to measure the dielectric properties in a limited area of a polymer using interdigitated comb sensors (a capacitor)
Applying an alternating electric field, the relative dielectric constant or permittivity of the polymer, associated with the mobility of the different types of dipoles, is measured.
The polymer is a dielectric characterized by a dielectric constant that depends on the amount and mobility of the dipoles present.
If the polymer absorbs water, the number of dipoles increases.
The H2O dipoles have a much higher mobility than those present in a glassy polymer.
~

## Slide 23: Indirect measurements of the concentration of water
Material: epoxy resin
Sample in the form of a thin film (0.8 mm) with the dielectric sensor in the middle.
~
X
The dielectric sensor has a thickness of about 30 mm.
The water absorption can be considered 1D in a system exposed from only one side B.C.: (¶c/¶x)x=0=0 (the sensor is impervious)
It is assumed that the variations of permittivity can be attributed solely to the fact that for x=0
x=0

## Slide 24: Indirect measurement of the concentration of water
The permittivity for x=0 increases during absorption
It may be assumed

## Slide 25: Indirect measurement of the concentration of water
In practice, it is assumed that the normalized concentration and the normalized permittivity are equal and then D can be computed from
Also in this case one a simplification can be made for low absorption times
t1/2= time for (C¥ -Co)/2, h= thickness

## Slide 26: Indirect measurement of the concentration of water
Once calculated D with the last simplified expression, it is possible to compare it with that one obtained from the weighing tests and simulate Mt/M¥

## Slide 27: Measure of water concentration in dough
Sensors and the circuit are DC.
The measure of current is performedfor a constant voltage of 1 V
It may be assumed as in the previous case

## Slide 28: Measure of water concentration in dough
The current measurements are sensitive to the variation of water content

## Slide 29: Measure of water concentration in dough
The dependence of the normalized current, I, as a function of by t0.5 indicates a Fickian behavior for a rubbery polymer: fresh pasta with bran consisting of hydrophilic polysaccharides

## Slide 30: Absoprtion of chloroform in syndiotactic polystyrene
Simultaneous thermal analysis TGA and DTA: the switch from a nitrogen atmosphere with a vapor of chloroform at 35 °C

## Slide 31: Absoprtion of chloroform syndiotactic in polystyrene
Simultaneous thermal analysis TGA and DTA: comparison of the absorption kinetics measured by the two techniques

## Slide 32
Permeability experiments
The amount of diffusing substance released at the low concentration side of a membrane, separating two environments at different concentrations, is measured.
Similarly to the previous case, in 1D geometry, the mass balance, initial conditions (IC) and boundary conditions (BC) are:
I.C. Ci(X,t)=Co t=0 x=[0,l]
B.C. C(X,t)=Co t>0 x=[l]
C(X,t)=C’o t>0 x=[0]
l
x
C’o
Co
Co
0

## Slide 33
Indicate by Qt the amount of mass that crosses the section at x=l
The solution of the mass balance for Co=0 is given as the sum of infinite terms:
The solution of the balance for t (steady state conditions) simplifies to:

## Slide 34
In steady state conditions the concentration profile is linear Jss=const
This equation represents the flow for unit area in steady state, and in a diagram Qt vs. t, is a straight line
For ideal Fickian systems, the time delay to reach the steady state is :
θ is known as time lag and can be used for an estimate of the of diffusion coefficient through a membrane of known thickness.
l
x
C’o
Co
Co
0
Qt

## Slide 35
In a permeability test, in the simplest case, the amount of gas Qt, which has crossed a membrane as a function of time, is determined by measuring the pressure in a chamber downstream and obtaining n =PV/RT or, for real gases, using other expressions
Qt
For any polymer, a linear concentration profile is attained across the thickness and at enough long times Qt becomes linear as a function of time.
Then a permeability value can be calculated as the ratio between the mass flow (in steady state in this case) and the pressure gradient:

## Slide 36
For ideal Fickian systems, if there is a linear concentration profile, then:
Jss=D(C’o-Co)/l
In a permeability test, in the simplest case, the amount of gas Qt, which has crossed a membrane as a function of time, is determined by measuring the pressure in a chamber downstream and obtaining n =PV/RT or, for real gases, using other expressions.
The amount that crosses the section A of the polymer in the time t, Qt, is:
The concentration of the penetrant which diffuses into the polymer is in equilibrium with the concentration of the penetrant in the surrounding medium (gas or vapor phase). For a gas:
Qt
slope

## Slide 37
Permeability results for a PolyImide membrane (Matrimid)

## Slide 38
Permeability experiments: dish method
The dish method is the simplest method also included in ASTM standard
A metal cup is sealed with the sample, a polymer film
50 RH% in the external environment is obtained using a controlled atmosphere and temperature oven
0% RH is obtained in the cup using a dessiccant (CaCl2)
The mass flow in steady state, Jss , is obtained as:
(amount of water absorbed by dessicant)/(time X sample area)=Qt/A t
CaCl2

## Slide 39: SUMMARY
Absorption test | Ideal Fickian | non-ideal Fickian | Non-Fickian (anomalous)
Mt/M ¥ vs t0.5 linear for Mt/M ¥<0.5 | Yes | Yes | (Yes/No)
ln(1-Mt/M ¥) vs. t linear | Yes | Yes | (Yes/No)
Overlapping absorpt. and desorb. plots | Yes | No | No
Crossing absorpt. and desorb. plots | No | No | Yes
Mt/M ¥ vs t0.5/l not dependent on l | Yes | No | No
Permeability test |  |  | 
Qt, linear at high t | Yes | Yes | Yes
D and S evaluable by Jss and q | Yes | No | No
q /l2 not dependent on l | Yes | No | No

## Slide 40: Diffusion: behavior for type of polymers
Rubbery Polymers (even amorphous phases of semicryst. polymers)
  Gas diffusion usually follows Fick’s law. (es. PE-O2)
  For vapours D and S can depend on C and therefore a non ideal Fickian behaviour is expected.
Glassy Polymers (even amorphous phases of semicryst. polymers)
  For gases at high pressure, D and S depend on C and hence a non ideal Fickian behaviour is expected
  When the solubility parameter of a vapour is close to that of the polymer, a structural change of the polymer is observed. D depends on time and from the space coordinate: non-Fickian behaviour or anomalous behaviour.

## Slide 41
Anomalous or non-fickian diffusion
In the limiting case of diffusion described by Fick's law, the initial stages of the absorption can be described by a relation type:
If the transport of matter is not controlled by diffusion phenomena, but only by changes of the physical state of the polymer, it falls in the other limiting case (called Case II). It can occur quite frequently in glassy polymers that, in the presence of a solvent, are swollen up, presenting a clear separation between the not penetrated polymer (still in the glassy state) and the swollen rubbery polymer.

## Slide 42
In the Case II the absorption kinetics are controlled by the slower of the two processes:
  Relaxation of the interface glassy-polymer/rubbery-polymer (the first is subject to tension from the second, which tends to swell)
  Transport (usually Fickian) of penetrating in the swollen rubbery layer
Swollen layer
(in compression)
Glassy layer
(in tension)
If the absorption is due to the advancement of the swollen front towards the glassy core not penetrated, the mass increase follows a linear law:

## Slide 43
Between the two extreme cases, fickian diffusion and Case II, intermediate cases are possible, then:
the value of the index n, is 0.5 for the diffusion controlled by Fick's law and 1 in the case of absorption controlled only by the relaxation (Case II).
In Case II the concentration profiles are typically:
x
Co
C’o
Rubbery swollen polymer
Glassy polymer
2l

## Slide 44
However, looking better the concentration profile, the region interested to the phase transition can have a finite thickness
x
Co
C’o
Rubbery swollen polymer
Zone of glass transition
Glassy polymer
In this example, the diffusive resistance of the rubbery layer may be negligible: control of the swelling Mt vs t linear
Co
C’o
x
In this example, the diffusive resistance of the rubbery layer controls the absorption Mt vs t0.5 linear
l
l

## Slide 45
a=D/(d(t) v)
Velocity v of swelling, cm/s
Diffusive conductance in the swollen layer:
D/d(t), cm/s
Swelling control
a>1 Mt vs t linear
Mt is controlled by the slowest process
Diffusive control
a<1 Mt vs t0.5 linear
time
swollen layer
glassy polymer
CASE II SORPTION

## Slide 46
Ultrasonic waves are mechanical vibrations that propagate in a polymeric material as a consequence of a series of very small continuous displacements of atoms and chain segments around their equilibrium positions.
The ultrasonic waves act as a high frequency dynamic mechanical deformation applied to the material.
The ultrasonic analysis is related to the small-scale mobility of short segments between entanglements.
Ultrasonic wave propagation in polymers
Notes: Because of the forces within a chain segment and between adjacent chain segments, displacements are induced at neighbouring zones and so on, thus propagating a stress-strain wave

## Slide 47
Ultrasonic parameters
VELOCITY: is related with the mechanical stiffness of the material.
It is calculated on the basis of the measured time of flight, that is the amount of time for the sound to travel through the sample.
d is the sample thickness
t is the time of flight
Notes: In an acoustic sense, a material is fully characterize by two parameters: the ultrasonic velocity v and the ultrasonic attenuation .
The US v is the velocity of propagation of elastic waves
The US v or the longitudinal modulus L’ can be considered the most interesting parameter for cure monitoring because it follows the growth and evolution of the mechanical stiffness of the resin during the cure.

## Slide 48
ATTENUATION: is a measure of the dissipative energy losses as the ultrasonic wave travels through the polymer, due to:
- absorption, aa
- scattering, as
It is calculated from the change in the amplitude of the acoustic signal.
a= (1/d)20 log(Ao/A) [dB/mm]
Ultrasonic parameters
d is the sample thickness
A0 is the amplitude of the reference echo
A is the amplitude of the actual echo
Through a material thickness x: A = Ao exp(-aax)
Notes: …converted to heat….. These energy losses are due to … … of ultrasonic waves
The scattering contribution is considerable when the medium is non-homogeneous and contains particles with a size comparable to the ultrasonic wavelength such as in filled polymers or sometimes in semicrystalline polymers.
The absorption is related to molecular rearrangements in the polymer structure, such as glass transition, melting, secondary transitions, and to chemical reactions such as the curing process.

## Slide 49
The ultrasonic wave propagation in polymers is related to their viscoelastic behaviour. When longitudinal waves are propagated:
L* = L’+ iL’’
where L’= K’+ 4/3 G’ and L’’= K’’+ 4/3 G’’
( if al/2p<<1 )
L” »2 rvL 2 (a/w)
Ultrasonic wave propagation in polymers
Notes: From measurements of longitudinal velocity v and attenuation α the component of the longitudinal modulus (here indicated easily with L’ and L’’) can be calculated according the following equations
When /2 <<1, i.e. when the attenuation per wavelength is small, as in most practical applications, the simplified formulas on the right can be used :

## Slide 50
Ultrasonic apparatus
Notes: The US apparatus used in this work is sketched in picture.
It consists of two ultrasonic transducers, fitted into the disposable tools of a parallel plate rheometer (Ares, Scientific Rheometric) and connected with a pulser-receiver card.
This latter generates a pulse train, amplifies the signal transmitted through the sample and provides an analogue/digital conversion of the signal, that, using a dedicated software, is sampled every 5s and displayed on the monitor of a PC.
The liquid resin sample is sandwiched between the delay lines of ultrasonic transducers, which are fitted within the rheometer oven. The resin thickness changes and the contact pressure are controlled by the vertical movement of the upper transducer, driven by the gap control function of the rheometer.

## Slide 51
Ultrasonic apparatus (UDMA)
Torque and axial force rheometer transducer
Rheometer oven
Rheometer tool
emitter/receiver
US receiver
US emitter
Reflection mode
Transmission mode
Notes: The US apparatus used in this work is sketched in picture.
It consists of two ultrasonic transducers, fitted into the disposable tools of a parallel plate rheometer (Ares, Scientific Rheometric) and connected with a pulser-receiver card.
This latter generates a pulse train, amplifies the signal transmitted through the sample and provides an analogue/digital conversion of the signal, that, using a dedicated software, is sampled every 5s and displayed on the monitor of a PC.
The liquid resin sample is sandwiched between the delay lines of ultrasonic transducers, which are fitted within the rheometer oven. The resin thickness changes and the contact pressure are controlled by the vertical movement of the upper transducer, driven by the gap control function of the rheometer.

## Slide 52
Ultrasonic transducers
A piezoelectric crystal (working up to 500 °C) is fitted in a probe fitting into the disposable tool of the Ares rheometer
f= 2-10 MHz
Transmission method
Oscilloscope output
A0
A1
A2
A0r
A1r
Piezoceramic transducer
(E)
(R)
Sample
Ultrasonic probe
Notes: The US transducers are made with piezoelectric crystals, which can work up 500 °C at the frequency of 2 MHz.
The photo shows the US transducers fitted into the rheometer disposable tools. The white part is the ceramic of the rheometer oven.
The picture on the left is the echogram in transmission mode.

## Slide 53
Ultrasonic transducers
Reflection method
h
A0
A1
A0r
A1r
Sample
Ultrasonic probe
Piezo crystal
Oscilloscope output
Notes: The US transducers are made with piezoelectric crystals, which can work up 500 °C at the frequency of Hz.
The photo shows the US transducers fitted into the rheometer disposable tools. The white part is the ceramic of the rheometer oven.
The picture on the left is the echogram in transmission mode.

## Slide 54
Water sorption in Poly(hema) hydrogels: weight gainapparent fickian behaviour
Notes: The evolution of the degree of reaction from DSC results as a function of the cure time has been compared in Fig.5 with another normalized degree of reaction calculated from ultrasonic data (US), according the following equation:
The degree of reaction DSC is calculated in isothermal DSC experiments according the first equation: …where H(t) represents the partial heat of reaction developed during an isothermal DSC experiment and HTOT is the maximum heat of reaction measured in non-isothermal experiments, taken as a reference value [
Indicating with max=HISO/HTOT the ratio between the heat developed during the isothermal (HISO) and scanning (HTOT) DSC experiments, it has been found that max is lower than 1 for all the investigated cure temperatures, which are lower than the maximum attainable glass transition temperature
At the beginning of the cure, as a consequence of the high concentration of reactive groups in the liquid reactive mixture, the degree of cure increases more rapidly than the ultrasonic longitudinal velocity vL, since the mechanical properties of the resin before the gel point are scarcely affected by the growth of the molecular weight. This is evident from the first part in the US curve. Close to gelation, the growing branched molecules present a considerable elastic response, detectable by a significant increase of L’. During the later stages of the cure, significant changes in US occur, while the degree of cure DSC is fully developed and nearly constant.

## Slide 55
Water sorption in hydrogels: reflection losses
Dry material
Water absorbing material
Saturated material
Transducer
c)
Transducer
d)
Transducer
a)
Transducer
b)
Sorption time
Notes: The evolution of the degree of reaction from DSC results as a function of the cure time has been compared in Fig.5 with another normalized degree of reaction calculated from ultrasonic data (US), according the following equation:
The degree of reaction DSC is calculated in isothermal DSC experiments according the first equation: …where H(t) represents the partial heat of reaction developed during an isothermal DSC experiment and HTOT is the maximum heat of reaction measured in non-isothermal experiments, taken as a reference value [
Indicating with max=HISO/HTOT the ratio between the heat developed during the isothermal (HISO) and scanning (HTOT) DSC experiments, it has been found that max is lower than 1 for all the investigated cure temperatures, which are lower than the maximum attainable glass transition temperature
At the beginning of the cure, as a consequence of the high concentration of reactive groups in the liquid reactive mixture, the degree of cure increases more rapidly than the ultrasonic longitudinal velocity vL, since the mechanical properties of the resin before the gel point are scarcely affected by the growth of the molecular weight. This is evident from the first part in the US curve. Close to gelation, the growing branched molecules present a considerable elastic response, detectable by a significant increase of L’. During the later stages of the cure, significant changes in US occur, while the degree of cure DSC is fully developed and nearly constant.

## Slide 56
Water sorption in hydrogels: reflection losses
Notes: The evolution of the degree of reaction from DSC results as a function of the cure time has been compared in Fig.5 with another normalized degree of reaction calculated from ultrasonic data (US), according the following equation:
The degree of reaction DSC is calculated in isothermal DSC experiments according the first equation: …where H(t) represents the partial heat of reaction developed during an isothermal DSC experiment and HTOT is the maximum heat of reaction measured in non-isothermal experiments, taken as a reference value [
Indicating with max=HISO/HTOT the ratio between the heat developed during the isothermal (HISO) and scanning (HTOT) DSC experiments, it has been found that max is lower than 1 for all the investigated cure temperatures, which are lower than the maximum attainable glass transition temperature
At the beginning of the cure, as a consequence of the high concentration of reactive groups in the liquid reactive mixture, the degree of cure increases more rapidly than the ultrasonic longitudinal velocity vL, since the mechanical properties of the resin before the gel point are scarcely affected by the growth of the molecular weight. This is evident from the first part in the US curve. Close to gelation, the growing branched molecules present a considerable elastic response, detectable by a significant increase of L’. During the later stages of the cure, significant changes in US occur, while the degree of cure DSC is fully developed and nearly constant.

## Slide 57
Water sorption in hydrogels: reflection losses
Notes: The evolution of the degree of reaction from DSC results as a function of the cure time has been compared in Fig.5 with another normalized degree of reaction calculated from ultrasonic data (US), according the following equation:
The degree of reaction DSC is calculated in isothermal DSC experiments according the first equation: …where H(t) represents the partial heat of reaction developed during an isothermal DSC experiment and HTOT is the maximum heat of reaction measured in non-isothermal experiments, taken as a reference value [
Indicating with max=HISO/HTOT the ratio between the heat developed during the isothermal (HISO) and scanning (HTOT) DSC experiments, it has been found that max is lower than 1 for all the investigated cure temperatures, which are lower than the maximum attainable glass transition temperature
At the beginning of the cure, as a consequence of the high concentration of reactive groups in the liquid reactive mixture, the degree of cure increases more rapidly than the ultrasonic longitudinal velocity vL, since the mechanical properties of the resin before the gel point are scarcely affected by the growth of the molecular weight. This is evident from the first part in the US curve. Close to gelation, the growing branched molecules present a considerable elastic response, detectable by a significant increase of L’. During the later stages of the cure, significant changes in US occur, while the degree of cure DSC is fully developed and nearly constant.

## Slide 58
Water sorption in hydrogels:attenuation
Notes: The evolution of the degree of reaction from DSC results as a function of the cure time has been compared in Fig.5 with another normalized degree of reaction calculated from ultrasonic data (US), according the following equation:
The degree of reaction DSC is calculated in isothermal DSC experiments according the first equation: …where H(t) represents the partial heat of reaction developed during an isothermal DSC experiment and HTOT is the maximum heat of reaction measured in non-isothermal experiments, taken as a reference value [
Indicating with max=HISO/HTOT the ratio between the heat developed during the isothermal (HISO) and scanning (HTOT) DSC experiments, it has been found that max is lower than 1 for all the investigated cure temperatures, which are lower than the maximum attainable glass transition temperature
At the beginning of the cure, as a consequence of the high concentration of reactive groups in the liquid reactive mixture, the degree of cure increases more rapidly than the ultrasonic longitudinal velocity vL, since the mechanical properties of the resin before the gel point are scarcely affected by the growth of the molecular weight. This is evident from the first part in the US curve. Close to gelation, the growing branched molecules present a considerable elastic response, detectable by a significant increase of L’. During the later stages of the cure, significant changes in US occur, while the degree of cure DSC is fully developed and nearly constant.

## Slide 59
Water sorption in hydrogels: velocity and modulus
Notes: The evolution of the degree of reaction from DSC results as a function of the cure time has been compared in Fig.5 with another normalized degree of reaction calculated from ultrasonic data (US), according the following equation:
The degree of reaction DSC is calculated in isothermal DSC experiments according the first equation: …where H(t) represents the partial heat of reaction developed during an isothermal DSC experiment and HTOT is the maximum heat of reaction measured in non-isothermal experiments, taken as a reference value [
Indicating with max=HISO/HTOT the ratio between the heat developed during the isothermal (HISO) and scanning (HTOT) DSC experiments, it has been found that max is lower than 1 for all the investigated cure temperatures, which are lower than the maximum attainable glass transition temperature
At the beginning of the cure, as a consequence of the high concentration of reactive groups in the liquid reactive mixture, the degree of cure increases more rapidly than the ultrasonic longitudinal velocity vL, since the mechanical properties of the resin before the gel point are scarcely affected by the growth of the molecular weight. This is evident from the first part in the US curve. Close to gelation, the growing branched molecules present a considerable elastic response, detectable by a significant increase of L’. During the later stages of the cure, significant changes in US occur, while the degree of cure DSC is fully developed and nearly constant.

## Slide 60
Water sorption in hydrogels: degree of crystallinity and thickness of the glassy core for PVA
Xg = (from ultrasonic measurements)
Xc = Crystallinity (from WAXD )
Notes: The evolution of the degree of reaction from DSC results as a function of the cure time has been compared in Fig.5 with another normalized degree of reaction calculated from ultrasonic data (US), according the following equation:
The degree of reaction DSC is calculated in isothermal DSC experiments according the first equation: …where H(t) represents the partial heat of reaction developed during an isothermal DSC experiment and HTOT is the maximum heat of reaction measured in non-isothermal experiments, taken as a reference value [
Indicating with max=HISO/HTOT the ratio between the heat developed during the isothermal (HISO) and scanning (HTOT) DSC experiments, it has been found that max is lower than 1 for all the investigated cure temperatures, which are lower than the maximum attainable glass transition temperature
At the beginning of the cure, as a consequence of the high concentration of reactive groups in the liquid reactive mixture, the degree of cure increases more rapidly than the ultrasonic longitudinal velocity vL, since the mechanical properties of the resin before the gel point are scarcely affected by the growth of the molecular weight. This is evident from the first part in the US curve. Close to gelation, the growing branched molecules present a considerable elastic response, detectable by a significant increase of L’. During the later stages of the cure, significant changes in US occur, while the degree of cure DSC is fully developed and nearly constant.